COLORFUL LED TUBE LIFT SYSTEM

User Manual

=======PROFESSIONAL LIGHTING EQUIPMENT========

NOTICED:DON’T USE THE MACHINE WITHOUT BALL

1.MENU KEY：

MENU           UP    DOWN   ENTR

Operation: Press the MENU key will cycle out different functions, press the key to adjust the up or down to modify its parameter values. Press the Enter button to confirm

2.Specification for Menu Key.

| NO | Display show | Specification |
| --- | --- | --- |
| 1 | DMX-MODE CH6/CH10 | Press the Up / Down key to switch 6/10 channel, press the OK Enter key to save |
| 2 | DMX-ADR 001 | Press the up and down keys to adjust the DMX512 address, press the Enter key to save. |
| 3 | ADJ－R 255 | Press the up and down keys to adjust the red brightness(0-255), press the Enter key to save. |
| 4 | ADJ－G 255 | Press the up and down keys to adjust the green brightness (0-255), press the Enter key to save。 |
| 5 | ADJ-B 255 | Press the up and down keys to adjust the blue brightness (0-255), press the Enter key to save。 |
| 6 | PROGRAM 001 | Press the up or down key to select the built-in program and press the Enter key to save. |
| 7 | SPEED 16 | Press the up or down key to select the built-in program speed (1-16)，press the Enter key to save. |
| 8 | TEST MODE | Press the up and down keys to enter sound and auto mode |
| 9 | RESET | Press enter Key to confirm the reset |

3．DMX512 Channal

6CH

| NO | Function | Specification |
| --- | --- | --- |
| 1CH | Red dimmer | Red dimming (0-255) linear dimming /from dark to light |
| 2CH | Green dimmer | Green dimming (0-255) linear dimming /from dark to light |
| 3CH | Blue dimmer | Blue dimming (0-255) linear dimming /from dark to light |
| 4CH | Dimmer | RGB dimming (0-255) linear dimming /from dark to light |
| 5CH | Strobe | （0－255）strober from slow to fast |
| 6CH | Light height | （0-255）adjust the height of the lift tube |

10CH

| NO | Function | Specification |
| --- | --- | --- |
| 1CH | Red dimmer | Red dimming (0-255) linear dimming /from dark to light |
| 2CH | Green dimmer | Green dimming (0-255) linear dimming /from dark to light |
| 3CH | Blue dimmer | Blue dimming (0-255) linear dimming /from dark to light |
| 4CH | Dimmer | RGB dimming (0-255) linear dimming /from dark to light |
| 5CH | Strobe | （0－255）strober from slow to fast |
| 6CH | Light height | （0-255）adjust the height of the lift tube |
| 7CH | Adjust lift speed | （0－255）Motor from fast to slow |
| 8CH | Built-in program | The first 7 channels are enabled (0-60); when DMX is More than 60, each built-in program is incremented by 17. |
| 9CH | Built-in program speed | 0-255 Upward speed slows down，0 is most quickly |
| 10CH | Sound-controlled/Auto and reset | (0-64) No function; (65-128) Auto; (129-192) Sound control; (193-255) Reset. Each function is delayed by 5 seconds. |

Turn on the power, when receiving the DMX512 signal, the LCD screen signal from the "X" to "V", at this moment ,can accept DMX control.

In the address code state, after the multi-machine connect together, if does not have the control with DMX, will enter the master slave model, operates one equipment, the rest in the address status equipment follows the host synchronization movement procedure. Connected to the console, in the address state of the device can be controlled by DMX control.

Specification

- Voltage: AC 90-240v, 50/60Hz
2. Power consumption: 140w
3. Lighting Source: 252pcs  led
4. Color: RGB

5. Control: DMX, master slave, sound active, auto mode.

7. Display: LCD display
8. N.W.: 9 kg
9. G.W.: 11 kg
10. Carton size: 430×310×400mm

4．Technical Index

Sound-active，build-in PRO，Master/Slave control。

strobe，program for choosing color，color changing。

256 high gray grade，0-100%dimmer