LED LASER BAR

- The illustration part：

A．Functional health

B．Add the healthy

C．Reduction of the healthy

D．Confirm the healthy

E．LED According to

2.LED display window function comparison table(all functions can be

confirmed by pressing the D key after selecting them)

| The serial number | According to | Functional specifications |
| --- | --- | --- |
| 1 | A001 | 24CH，（001—512） B, C key plus or minus address code value |
| 2 | d001 | 8CH，（001—512） B, C key plus or minus address code value |
| 3 | FF00 | Effect of change， （01—99） B, C key to modify the running speed |
| 4 | BEB1 | Voice control effects change__1 |
| 5 | BEB2 | Voice control effects change__2 |

3．DMX512    24Channel show

| The serial number | function | instructions |
| --- | --- | --- |
| 1 channel | Tuned light | 0--255 Laser 1-8 total modulation, from dark to light 0-100%; |
| 2 channel | Laser 1dimming | The laser brightness ranges from 0 to 100% |
| 3channel | Laser 2dimming | The laser brightness ranges from 0 to 100% |
| 4 channel | Laser 3dimming | The laser brightness ranges from 0 to 100% |
| 5 channel | Laser 4dimming | The laser brightness ranges from 0 to 100% |
| 6 channel | Laser 5dimming | The laser brightness ranges from 0 to 100% |
| 7 channel | Laser 6dimming | The laser brightness ranges from 0 to 100% |
| 8 channel | Laser 7dimming | The laser brightness ranges from 0 to 100% |
| 9 channel | Laser 8dimming | The laser brightness ranges from 0 to 100% |
| 10 channel | LED1 dimmer | LED brightness ranges from 0 to 100% |
| 1 1channel | LED2 dimmer | LED brightness ranges from 0 to 100% |
| 12 channel | LED3 dimmer | LED brightness ranges from 0 to 100% |
| 13 channel | LED4 dimmer | LED brightness ranges from 0 to 100% |
| 14 channel | LED5 dimmer | LED brightness ranges from 0 to 100% |
| 15 channel | LED6 dimmer | LED brightness ranges from 0 to 100% |
| 16channel | LED7 dimmer | LED brightness ranges from 0 to 100% |
| 17 channel | LED8 dimmer | LED brightness ranges from 0 to 100% |
| 18 channel | Total stroboscopic | 0--255Laser -LED 1-8 total strobe, from slow to fast 0-100%; |
| 19 channel | The motor position | Motor scanning position |
| 20channel | Motor position adjustment | Motor scanning position adjustment |
| 21channel | Motor swing | 0-20 no, 21-255 (0-180 degrees) speed from fast to slow |
| 22 channel | Motor reset | 0-50 no, 51-100 positioning center, 101-255 no |
| 23 channel | Feature selection | 0--35： no； 36--45： Jump run pattern 1(motor controlled); 116--125：Jump run pattern 8(motor controlled); 126--135：Voice control 1(motor controlled); 136--145：Voice control 2(motor controlled); 146--155：Jump change running pattern 1(motor automatic); 226--235：Jump run pattern 8(motor automatic); 236--245：Voice control 1(automatic motor); 246--255：Voice control 2(automatic motor); |
| 24 channel | Functional speed | Function speed from slow to fast |

4．DMX512    8Channel show

| The serial number | function | instructions |
| --- | --- | --- |
| 1 channel | Tuned light | 0--255 Laser 1-8 total modulation, from dark to light 0-100%; |
| 2 channel | Total stroboscopic | 0--255Laser -LED 1-8 total strobe, from slow to fast 0-100%; |
| 3 channel | The motor position | Motor scanning position |
| 4channel | Motor position adjustment | Motor scanning position adjustment |
| 5channel | Motor swing | 0-20 no, 21-255 (0-180 degrees) speed from fast to slow |
| 6 channel | Motor reset | 0-50 no, 51-100 positioning center, 101-255 no |
| 7 channel | Feature selection | 0--35： no； 36--45： Jump run pattern 1(motor controlled); 116--125：Jump run pattern 8(motor controlled); 126--135：Voice control 1(motor controlled); 136--145：Voice control 2(motor controlled); 146--155：Jump change running pattern 1(motor automatic); 226--235：Jump run pattern 8(motor automatic); 236--245：Voice control 1(automatic motor); 246--255：Voice control 2(automatic motor); |
| 8 channel | Functional speed | Function speed from slow to fast |

5．Working mode：

1. Please read the instructions carefully before using the product

2. Do not disassemble the laser lamp without permission. It should be repaired by

professional staff.

3. Use in dry and ventilated indoor environment to prevent vibration and impact.

4. Please don't look directly at the laser

- Playful working mode：voice control, self - paced, DMX signal control

- LASER：Blue1000mW*8+3W LED

◆	Enter voltage：AC 110V~240V  50/60Hz

◆	Power：150W

◆	The work environment：10℃ ~ 35℃